## Slide 1: CE461- COMPUTER APPLICATIONS IN FOUNDATION ENGINEERING
Immediate Settlement of Foundations on Clay

## Slide 2
Immediate settlement:
Si = μ0.μ1.q.B/E
Si : immediate settlement on clay (mm)
q : average applied vertical pressure (kPa)
B : width of the foundation (m)
E : modulus of elasticity of the soil (MPa)

## Slide 3
μ0 and μ1 are empirical factors dependent on foundation geometry and depth (dimensionless parameters).

## Slide 4
D : depth of the foundation (m)
H : the vertical distance between hard stratum and the base of the
foundation (m)
L : length of the foundation (m)

## Slide 5
Janbu, Bjerrum and Kjaernsli (1956)

## Slide 6
Chart: D/B
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
mü0 | 1 | 0.91 | 0.89 | 0.88 | 0.875 | 0.87 | 0.869 | 0.867 | 0.865 | 0.863 | 0.861 | 0.8608 | 0.8605 | 0.8603 | 0.8601 | 0.86 | 0.86 | 0.86 | 0.86 | 0.86 | 0.86
Janbu, Bjerrum and Kjaernsli (1956)
Excel drawing to obtain μ0

## Slide 7
Chart: H/B
| 0.1 | 0.3 | 0.6 | 0.9 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 1000
mü1iki | 0 | 0.1 | 0.2 | 0.305 | 0.35 | 0.6 | 0.705 | 0.79 | 0.82 | 0.85 | 0.88 | 0.9 | 0.9 | 0.9 | 0.93 | 0.94 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95
mü1squareya | 0 | 0.1 | 0.2 | 0.29 | 0.35 | 0.5 | 0.58 | 0.61 | 0.63 | 0.65 | 0.66 | 0.67 | 0.68 | 0.69 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.7 | 0.71
mü1circla | 0 | 0.1 | 0.2 | 0.29 | 0.35 | 0.48 | 0.52 | 0.56 | 0.58 | 0.59 | 0.6 | 0.6 | 0.605 | 0.61 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63 | 0.63
mü1beslik | 0 | 0.1 | 0.2 | 0.305 | 0.35 | 0.6 | 0.8 | 0.9 | 1 | 1.05 | 1.09 | 1.105 | 1.13 | 1.15 | 1.24 | 1.28 | 1.3 | 1.31 | 1.32 | 1.33 | 1.34 | 1.35 | 1.35 | 1.37 | 1.38 | 1.39 | 1.39
mü1onluk | 0 | 0.1 | 0.2 | 0.305 | 0.35 | 0.6 | 0.8 | 0.9 | 1.1 | 1.18 | 1.21 | 1.25 | 1.29 | 1.43 | 1.5 | 1.54 | 1.57 | 1.59 | 1.6 | 1.6 | 1.605 | 1.61 | 1.65 | 1.67 | 1.68 | 1.69 | 1.69 | 1.69 | 1.695 | 1.695 | 1.695
mü1infinitli | 0 | 0.1 | 0.2 | 0.305 | 0.35 | 0.6 | 0.8 | 0.9 | 1 | 1.1 | 1.19 | 1.26 | 1.31 | 1.34 | 1.5 | 1.63 | 1.7
Janbu, Bjerrum and Kjaernsli (1956)
Excel drawing to obtain μ1

## Slide 8
Clay layers
Water table at ground surface
In calculation of the shape factors (μ0 and μ1), curve are fitted in excel and equations of these curve are used in the code.
Foundation rigidity and depth factors are not applied to this calculation.
Principle of superposition
A guide for CE366 Foundation Engineering I students
General Considerations

## Slide 10: What I Did?
Immediate settlement were determined.
A simple hand design were done.
Different and found formulations were brought together in MATLAB GUI.
Algorithm was developed, and coded.