## Slide 1: Marmaray Feneryolu Station
November 9, 2016
YEGOO DESIGN

## Slide 2: Outline
Introduction
Design Criteria
Roof Design
Slab Design and Alternatives
Column Design
Geotechnicalical Properties and Foundation Design

## Slide 3: INTRODUCTION

## Slide 4: Project in numbers
Total length: 76.6 km
Total stations: 40
Passengers per hour : 75,000
Target: 1.5 million passengers per day

## Slide 5: Location
(https://upload.wikimedia.org/wikipedia/commons/0/0f/Marmaray_Istanbul_Project.png)

## Slide 6: Kadıköy – Feneryolu Marmaray Station
(https://www.google.de/maps/place/Feneryolu/@40.9794607,29.045282,877m/data=3m2!1e3!4b1!4m5!3m4!1s0x14cac780c8073283:0xf951677e7d96b385!8m2!3d40.9794607!4d29.0474707!)

## Slide 7: 3D VIEW

## Slide 8: Section View

## Slide 9: Side View

## Slide 10: DESIGN CRITERIA

## Slide 11: Design Criteria
DISCIPLINE | STANDARDS
GENERAL | TS-TURKISH STANDARDS
LOADING | TS498-DESIGN LOADS FOR BUILDING TSC2007-TURKISH SEISMIC CODE TURKISH STATE METEOROLOGICAL SERVICE
CONCRETE DESIGN | TS500-REQUIREMENTS FOR DESIGN AND CONSTRUCTION OF REINFORCED CONCRETE STRUCTURES TSC2007-TURKISH SEISMIC CODE
STEEL DESIGN | DESIGN AND CONSTRUCTION SPECIFICATIONS FOR STEEL STRUCTURES by MINISTIRY OF ENVIORENMENT AND URBAN PLANNING (September, 2016)

## Slide 12: Material properties
C30 and S420a
Material factors for Concrete Design
  Concrete 1.5
  Steel 1.15
S275 and S355 steel members

## Slide 13: Design Criteria
Concrete
Ultimate Strength Design (USD)
Steel
Load and Resistance Factor Design (LRFD)

## Slide 14: Loads Acting on the Structure
Dead load (G)
Self weight
Additional Dead Loads
Live load (Q)
Roof live load
Floor live load
Snow load (S)
Wind load (W)
Earthquake load (E)
Temperature load (T)

## Slide 15
DISCIPLINE | LOAD COMBINATION | SOURCES
CONCRETE DESIGN (ULTIMATE STRENGTH DESIGN) | 1.4G+1.6Q | TS500 TSC2007 Design and Construction Specifications for Steel Structures by Ministry of Environment and Urban Planning (September, 2016)
 | 1.0G+1.2Q+1.2T | 
 | 1.0G+1.3Q+1.3W | 
 | 0.9G+1.3W | 
SEISMIC DESIGN | G+Q±Ex±0.3Ey | 
 | G+Q±Ey±0.3Ex | 
 | 1.0G+1.0Q+1.0E | 
 | 0.9G+1.0E | 
 | 1.2G+1.0Q+0.2S+1.0E | 
STEEL DESIGN (LOAD AND RESISTANCE FACTOR DESIGN) | 1.4G | 
 | 1.2G+1.6Q+0.5(Qr or S) | 
 | 1.2G+1.6(Qr or S) +(Q or 0.8W) | 
 | 1.2G+1.0Q+0.5(Qr or S) +1.6W | 

## Slide 16: ROOF DESIGN

## Slide 17: Roof Plan Layout

## Slide 18: Section A-A & D-D

## Slide 19
Pratt Truss System
Bottom Chord 2 UPN160
Top Chord 2 UPN140
Diagonals 2L 70x70x10

## Slide 20: SLAB DESIGN and ALTERNATIVES

## Slide 22
Beam - Slab Plan

## Slide 23
DÜZELTİLCEK

## Slide 24: Precast - Slab

## Slide 25
(http://www.pbprefabrik.com.tr/assets/documents/bdp.jpg)

## Slide 26: Hollow-core slab (precast)
Lower self weight
Less material
Higher load carrying capacity
Mass production opportunity
Not affected by severe climate conditions

## Slide 27: COLUMN DESIGN

## Slide 28
Ground Floor Columns

## Slide 29
Nd ≤ 0,9 * fcd * Ac for TS500
Nd ≤ 0,75 * fcd * Ac for Turkish Seismic Code
Min
Cross sectional area for one column (D=1.0 m) Ac = 785000 mm2 > min Ac

## Slide 30: First Floor Columns (Steel Column Case)

## Slide 31: First Floor Columns (R.C. Case)

## Slide 32: GEOTECHNICAL PROPERTIES and FOUNDATION DESIGN

## Slide 33: Site Investigation
I.Boreholes
No. Of Borehole (BH) | Depth (m)
BH-1 | 30.00
BH-2 | 25.00
BH-3 | 30.00
BH-4 | 25.00
BH-5 | 30.00
BH-6 | 25.00
BH-7 | 25.00
BH-8 | 30.00
BH-9 | 15.00

## Slide 34
II. Soil Parameters
Description | cu (kPa) | Фu | c’ (kPa) | Ф’ | ɣ (kN/m3) | mv (m2/kN) | Eu (kPa)
Silty Clay | 200 | 0 | 15 | 28 | 18.5 | 0.40*10-4 | 45000
Group Symbol | Clay (CH, CL) & Silt (MH, ML)
Water Content | w(%) = 15.2 – 40.9 => Estimated Value of w(%) = 26.0
Plasticity Index | PI(%) = 50.8 – 96.3 => Estimated Value of F(%) = 23.0
UnitWeight (kN/m3) | ɣ(%) = 16.07–20.30 => Estimated Value of ɣ(%) = 18.5 kN/m3

## Slide 35: III. Idealized Soil Profile
    Nort = 50
    Stiff Soil No ground improvement

## Slide 36: IV. Foundation Type
Type | Continuous Foundation
Width | 10.0 m
Thickness | 0.50 m
Length | 59.80 m
Area | 10*59.80 = 598 m2

## Slide 37: Bearing Capacity
Structure | Type of Foundation | B*L (m) | Nc | cu(kPa) | (qnet)safe (kPa) | ɣ*Df | (qtotal)safe (kPa)
Marmaray Station (on 4 platforms) | Continuous Foundation | 10.0* 59.8 | 5.2 | 200 | 347 | 37 | 384
Settlement
Stotal = 0.089 cm acceptable

## Slide 38: Cost Estimation
 | m2 | Cost
Platform Area | 2167 | TRY 1,993,640.00
Concourse Area | 3308 | TRY 3,043,360.00
Roof Area | 3587 | TRY 3,300,040.00
 | Total | TRY 8,337,040.00
Unit price for a metro station 920,00 TL/m2

## Slide 39: References
Birand,A., Ergun, U., & Erol, O. (2011). CE366 Foundation Engineering 1 Lecture Notes.
Carter, M., & Bentley, S. P. (1991). Correlations of Soil Properties. London: PENTECH PRESS.
CE363 Lecture Notes.
CE464 Lecture Notes.
DESIGN AND CONSTRUCTION SPECIFICATIONS FOR STEEL STRUCTURES by MINISTIRY OF ENVIORENMENT AND URBAN PLANNING (September, 2016)
Ersoy, U., Özcebe, G., & Tankut, T. Reinforced Concrete. Ankara: METU Press.
TS498-DESIGN LOADS FOR BUILDING.
TS500-REQUIREMENTS FOR DESIGN AND CONSTRUCTION OF REINFORCED CONCRETE STRUCTURES
TSC2007-TURKISH SEISMIC CODE.

## Slide 40
QUESTIONS ?
THANK YOU…