## Slide 1: MIDDLE EAST TECHNICAL UNIVERSITY DEPARTMENT OF CIVIL ENGINEERING
CE 410
CIVIL ENGINEERING DESIGN
DESIGN OF WASTEWATER AND STORMWATER
SYSTEMS OF ARSİN, TRABZON

## Slide 2
Outline
1. Introduction
2. Population Estimation
3. Wastewater Quantity
4. Selected Area
5. Pump Station
6. Storm Water Drainage
7. Conclusion
8. References

## Slide 3: Arsin
A coastal town in Trabzon (7 kilometer coastline)
Central and Rural Areal sum of 180 km2
Population of 18,000 (Central)
Main sources of income are from livestock and hazelnut
Hosts an Industrial Site

## Slide 4: Population Estimation
Chart: Population Census Results between the years 1965-2009
| 1965 | 1970 | 1975 | 1980 | 1985 | 1990 | 2000 | 2007 | 2008 | 2009
1965 1970 1975 1980 1985 1990 2000 2007 2008 2009 | 4028 | 4517 | 6557 | 6892 | 6479 | 6705 | 13038 | 8453 | 10715 | 10395

## Slide 5: Population Extrapolation Methods
Arithmetic Extrapolation
Geometric Extrapolation
Turkish Bank of Provinces Method
Logistic S Curve Method
Declining Growth Rate Method

## Slide 6
Chart: Population Calculation Curves
| 1965 | 1970 | 1975 | 1980 | 1985 | 1990 | 2000 | 2007 | 2008 | 2009 | 2011 | 2012 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
The Arithmetic Extrapolation Method | 4028 | 4517 | 6557 | 6892 | 6479 | 6705 | 13038 | 8453 | 10715 | 10395 | 17389 | 17366 | 18024 | 19120 | 20216 | 21312 | 22408 | 23504 | 24600 | 25696
The Geometric Extrapolation Method | 4028 | 4517 | 6557 | 6892 | 6479 | 6705 | 13038 | 8453 | 10715 | 10395 | 17389 | 17366 | 18713 | 21194 | 24004 | 27187 | 30791 | 34874 | 39497 | 44734
The Turkish Bank of Provinces Mehod | 4028 | 4517 | 6557 | 6892 | 6479 | 6705 | 13038 | 8453 | 10715 | 10395 | 17389 | 17366 | 17893 | 18805 | 19765 | 20773 | 21832 | 22946 | 24116 | 25347
Logistic S-Curve Method | 4028 | 4517 | 6557 | 6892 | 6479 | 6705 | 13038 | 8453 | 10715 | 10395 | 17389 | 17366 | 19670 | 19717 | 19741 | 19753 | 19760 | 19763 | 19765 | 19766
Declining Growth Rate Method | 4028 | 4517 | 6557 | 6892 | 6479 | 6705 | 13038 | 8453 | 10715 | 10395 | 17389 | 17366 | 19267 | 19470 | 19590 | 19662 | 19704 | 19730 | 19745 | 19754

## Slide 7
Population Estimation= 30,000

## Slide 8: ESTIMATING WASTEWATER QUANTITY

## Slide 9: BANK OF PROVINCES SPECIFICATIONS

## Slide 10: POPULATION VERSUS DAILY DEMAND
Population | Daily water demand (lt/day/cap)
0-3000 | 60
3000-5000 | 60-80
5000-10000 | 70-80
10000-30000 | 80-100
30000-50000 | 100-120
50000-100000 | 120-170

## Slide 11: DIVISION OF ARSIN REGION

## Slide 12: REGIONS OUTPUT DISCHARGES
 | Region I | Region II | Region III | Total
Coast (m) | 1203.5 | 3060 | 720 | 4983.5
Area (ha) | 57.52 | 190.00 | 54.97 | 302.49
Population (p/ha) | 90 | 100 | 75 | 99.18
Population (p) | 5177 | 19000 | 6523 | 30700
Discharge (lt/s) | 11.98 | 43.98 | 15.10 | 71.06

## Slide 13: REGIONS OUTPUT DISCHARGES

## Slide 15: SLOPE PROVISIONS OF BANK OF PROVINCES
Diameter (mm) | Slope | Max Discharge (lt/s) | Velocity(m/s)
150 | 1/150 | 20,21 | 1,143
200 | 1/200 | 37,69 | 1,2
250 | 1/250 | 61,12 | 1,245
300 | 1/300 | 90,72 | 1,283
400 | 1/400 | 169,21 | 1,347
500 | 1/500 | 274,41 | 1,398

## Slide 16: ROUGH ESTIMATION OF MAIN PIPES DIAMETER BETWEEN STATIONS
Pipe | Pipe Length (m) | Region | Rise Point Gap (m) | # of Rise
250 mm Pipe Distance From 0 | 1610 | I&II | 1000 | 1
250 mm Pipe Distance From 1610 m | 1700 | II | 1250 | 1
300 mm Pipe Distance From 3310 m | 1020 | II | 1500 | 0
200 mm Pipe Distance From 4330 m | 650 | III | 1000 | 0

## Slide 17: Selected Area
In the second region
Area of 65 hectars
Population of 6500
Limited by water-stream from the east
Includes one pump station placed by the main line

## Slide 18
Flow Directions by Streets

## Slide 19: Detailing
Conduits
Manholes
Elevations
Flow-Flaps
What are shown?

## Slide 20: External Flows
Using the formula;
External flows entering the region
have been calculated.

## Slide 21: Pump Station
To transmit water further
To transmit water to an upper elevation
To avoid deep excavations in wastewater transmission line

## Slide 22: Diameter and Slope Relation in Pipe Lines
Çap (mm) | Minimum Eğim | Maksimum Eğim | Doluluk oranı % | Max.baca aralığı (m)
 200 | 300 | 7 | 40 | 60
 300 | 500 | 7 | 50 | 60
 400 | 600 | 25 | 60 | 70
 500 | 800 | 25 | 60 | 70
 600 | 1000 | 25 | 60 | 70
 800 | 1200 | 50 | 60 | 80
 1000 | 2000 | 75 | 70 | 100
 1200 | 2050 | 75 | 70 | 125
 1400 | 2100 | 75 | 80 | 150
 1600 | 2150 | 75 | 80 | 150
 2000 | 2250 | 75 | 80 | 150
 3000 | 2500 | 75 | 80 | 150

## Slide 23: Discharges for Different Years
 | Q37 (lt/sec) | Q18 (lt/sec) | Q12 (lt/sec)
10 Years | 4,97 | 10,21 | 15,32
25 Years | 5,81 | 11,95 | 17,93
35 Years | 6,89 | 14,16 | 21,24

## Slide 24: Pump Discharges and Pump Powers for years 2025,2040 and 2050
Year | Pump Type | Main Pump (Number) | Backup Pump (Number) | Discharge (lt/sec) | Pump Power (kW)
2025 | Submerged Pump | 2 | 1 | 12 | 5,5
2040 | Submerged Pump | 2 | 1 | 12 | 5,5
2050 | Submerged Pump | 2 | 1 | 12 | 5,5

## Slide 25: Dimensions and Elevations of Waste Water Gathering Room
Height = 7.5 m
Length = 4 m
Width = 3 m
Pump axis elevation = -1.749 m
Base elevation of waste water gathering room = -2.03 m
Ground elevation of pump station = +5 m

## Slide 26: Location of the Pump Station

## Slide 27: Storm Water

## Slide 28: Storm Water in Nature

## Slide 29: Storm Water in Urban

## Slide 30: Problems of run-off water
Floods
Water pollution
Serviceability

## Slide 31: Storm Water Drainage System

## Slide 32: Design Criteria
Manholes & Pipes Placement
Discharge calculations using rational equation
-
where C: run-off coefficient
I: Rainfall Density
A: Basin Area
Manning Equation

## Slide 33: Conclusion
Research on area
Calculation of population
Specify the general system
Detailed placement on selected area
Pump station design
Storm water pipeline

## Slide 34: What is next?
Detailed Pump Design
  Calculations of valves and waterhammer
Storm water calculations
  Pipe diameters
  Discharge on each pipe
Detailed design of wastewater network
  Pipe diameters
  Discharges on each pipe
Cost Estimation

## Slide 37
http://www.worldbank.org/
http://www.dizayngrup.com/
http://www.ilbank.gov.tr/
http://www.61saat.com/bolgesel/arsin-osb-de-istihdam-ve-ihracat-rakamlari-aciklandi-h241734.html
http://www.ajanstrabzon.com/davutoglu-arsinin-onunde-yatirim-adasi-kuruyoruz.html
http://www.haberx.com/bakan_isik_arsinde_yatirim_adasini_gorusecek%2817,n,12044910,494%29.aspx
http://www.haber711.com/trabzon-turizmi-gelisiyor/
http://trabzon.tarim.gov.tr/Haber/66/Ilimiz-Projelerle-Gelisiyor
References