## Slide 1: DesIgn of HIghway BrIdge

## Slide 2: OutlIne
Introduction
Deck Design
Pier Design
Geotechnic Design
Cost Estimation

## Slide 3: IntroductIon
Iraq
Mosul
Great Zab River
LOCATION

## Slide 4: IntroductIon
L=240 m
W=15 m
2 lane highway

## Slide 5: STRUCTURAL DesIgn OF DECK and analysıs
Arslan AGAMURADOV

## Slide 6: DesIgn crIterIa and codes
AASHTO: The American Association of State Highway and Transportation Officials
SSHB: Standart Specifications for Seismic Design of Highway Bridges
ACI: American Concrete Institute
US system was changed to SI

## Slide 7: External dead loads (DL)
Load coming from the aspahlt layer:
Asphalt area= 15*0.06=0.9m2
Asphalt density=21 kN/m3
0.9*21=18.9 kN/m
Loads coming from the guardrails:
Pedestrian guardrail =1 kN/m
Guardrail = 4 kN/m
4+1= 5 kN/m Total external dead loads= 23.9 kN/m

## Slide 8: Total external vertIcal Loads
Truck loads, External live loads (LL):
W2= 300/20= 15 kN/m
Brake loads from Truck (AASHTO 3.9)
2.5 kN/m
Live loads :15+2.5=17.5 kN/m
Total External Loads:
15+2.5+23.9 = 41.4 kN/m

## Slide 9: WInd loads (AASHTO 3.15)
Wind speed : 45km/hr
Wind load acting from the side, qw,T : 2.4 kN/m2

## Slide 10: Cross-sectIon SelectIon: Support Section

## Slide 11: Cross-sectIon SelectIon: MId-span

## Slide 12: Diaphragms in support cross-section
Diaphragm load is taken as 450 kN/m to each side of the support for 2 meters.
Diaphragms are essential for resisting high shear stresses at supports.

## Slide 13: Cross-sectional properties
 | Shape | Name | Area m2 | Ix m4 | Iy m4 | Iz m4 | Cyp m | Cym m | Czp | Czm
PSC | 1CEL | SUPPORT | 12.14 | 87.80 | 39.76 | 207.68 | 7.50 | 7.50 | 1.99 | 2.51
PSC | 1CEL | SPAN | 10.04 | 24.61 | 9.03 | 160.26 | 7.50 | 7.50 | 1.04 | 1.36
Tapered | 1CEL | ss | 12.14 | 87.80 | 39.76 | 207.68 | 7.50 | 7.50 | 1.99 | 2.51
Tapered | 1CEL | ss2 | 10.04 | 24.61 | 9.03 | 160.26 | 7.50 | 7.50 | 1.04 | 1.36
DB/User | SR | column | 3.14 | 1.57 | 0.79 | 0.79 | 1.00 | 1.00 | 1.00 | 1.00

## Slide 14: Finalized deck
Profile View of River bed
MIDAS modeled deck

## Slide 15: Material Selection and deck load
Concrete: C50 γc= 25kN/m3
Steel Reinforcement: S420 γs= 78.5 kN/m3
Dead Load coming From the deck structure (uniform distribution)
P=64000 kN W= 64000/240 =267 kN/m
Load Combination AASHTO 3.22: 1.0(DL)+1.0(LL) + 1.0(D) + 1.0(W)
Total distributed load: 267+ 41.4 =308.4 kN/m

## Slide 16: Moments From Loads

## Slide 17: Moments From Loads
Moments at midspan:Moments at first and last spans:
Mm1=Mm2= 7.89e+4 kN.m
Moments acting on 2nd and 3rd spans:
Mm2=Mm3=4.59e+4 kN.m
Moments acting on supports:
Ms1= -8.62e+4 kN.m
Ms2= -6.96e+4 kN.m
Ms3= -1.03e+5 kN.m

## Slide 18: Stresses Acting on the Deck
Under NA
Above NA

## Slide 19: Stresses Acting on the Deck
Name | Top Part (kN/m2) | Bottom part (kN/m2)
Span 1 | -8.53e+3 | 1.58e+4
Span 2 | -4.81e+3 | 9.97e+3
Span 3 | -4.81e+3 | 9.97e+3
Span 4 | -7.29e+3 | 9.97e+3
Support 1 | 5.12e+3 | -5.67e+3
Support 2 | 3.88e+3 | -5.67e+3
Support 3 | 5.12e+3 | -5.67e+3

## Slide 20: Tendon installation and Post-tensioning
At mid-span:
σt=+ -
At support:
σt= + -
Cable material used: 19C15 cables
fs= 1860 Mpa
Ф= 15mm
# of wires= 19

## Slide 23: Cabling detail
In total 16*4+4*4= 80 cables
16 along each span
4 on each mid-span in blisters

## Slide 24: Tendon installation and Post-tensioning
Post-tensioning up to75% of yield strength of the cable

## Slide 25: Stresses after post-tensioning
Under NA
Above NA

## Slide 26: Stresses after post-tensioning
Name | Top Section (kN/m2) | Bottom Section (kN/m2)
Span 1 | -1.67e+4 | -6.05e+4
Span 2 | -1.51e+4 | -4.84e+4
Span 3 | -1.67e+4 | -4.84e+4
Span 4 | -2.16e+4 | -6.05e+4
Support 1 | -3.72e+3 | -5.44e+4
Support 2 | -3.72e+3 | -6.05e+4
Support 3 | -3.72e+3 | -5.44e+3

## Slide 27: DesIgn and Construction of PIers
Can Özsoy

## Slide 28: ConstructIon of PIers
2 piers’ foot naturally dried
Third pier artifically dried

## Slide 29: BearIng System

## Slide 30: Earthquake
AASHTO LRFD Bridge Design
Deprem Bölgelerinde Yapılacak Binalar Hakkında Esaslar
A0=0.3
T=2.56
Soil Classification = S2
Total Weight=70000 kN
1G+1Q+1E

## Slide 31: Earthquake
-Earthquake response coefficient=0.022
-Single Mode Analysis
-Uniform Load Method
-Fx=80.25 kN
-Fy=80.25 kN

## Slide 32: DesIgn of PIers
TS500
Nd=9800 kN
Vd=80.25 kN
Md=501.56 kN
=1.06 mm
C50
S420

## Slide 33: Cross-Section
D=2 m

## Slide 34: Cross-Section
-12 stirrups
-s=70 mm
-s=35 mm

## Slide 35: GEOTECHNICAL DESIGN
Load combInatIons
FoundatIon system
Foundation pressures
SoIl profIlE
Settlements
B.C.
Pile design
Efkan Evkuran

## Slide 36
Load combination
(1.0) * D + (1.0) * L + (1.0) * E
2. Foundation system
GEOTECHNICAL DESIGN

## Slide 37
3. Total and Net Foundation Pressures
1280 tons from structure
Weight of the raft = 12 * 12 * 2 * 2.5 = 720 tons
Total weight that is transmitted to the soil = 1280+720= 2000 tons
4. Soil profile
GEOTECHNICAL DESIGN

## Slide 38
Net foundation pressure
The weight of excavated soil = 12*12*2*19=5472 kN
qnet = (Total weight – excavated soil) / (B*L) = (20000-5472) / (12 * 12)
qnet = 101 kPa
5. Settlements
Immediate settlement
Si = 0 * 1 * q * B / E
GEOTECHNICAL DESIGN

## Slide 39
D/B = 2/12 = 0.17
0 = 1.0
H/B = 10/12 = 0.83
L/B = 12/12 = 1
1 = 0.25
S = 1.0 * 0.25 * 101 * 12 / 800
= 0.379 m = 38 cm
GEOTECHNICAL DESIGN

## Slide 40
6. Ultimate capacity
qf = (1 / 2) * sγ * γ * B * Nγ + sc * c * Nc + sq * γ * D *Nq
qf = ( 1 / 2 ) * 0,8 * 19 * 12 * 19 + 1 * (19) *2*19= 2455 kPa
2455 / (101) = 24 > 3,0
GEOTECHNICAL DESIGN

## Slide 41
7. Pile design
Skin friction
For 8 m alluvium layer,
(19-9.81)*8/2 = 36.7 kPa
Qsg = 3.14*6.7*8 = 168 kN = 17 tons
For 8.0-20.0m claystone
Qf = 3.14*0.21*400*12 = 3165 kN = 317 tons
Cumulative Skin Friction, Qs = 17+317 = 334 tons
GEOTECHNICAL DESIGN

## Slide 42
End bearing
For side friction F.S.= 2 and for end bearing F.S.=3
Qall=(282.6/3)+(334/2) = 261.2 tons = 2612 kN
Number of piles
Each pile diameter is estimated as 1 m.
GEOTECHNICAL DESIGN

## Slide 43
Pile Group Capacity
Qag = N * Qall * number of piles
Qag is allowable group capacity.
N, efficiency = 1 - arctan(D/s) * [ (m-1) * n + (n-1) * m ] / ( 90 * m * n )
m = 4 and n = 2
N = 0.63
Qag = 13164 kN
GEOTECHNICAL DESIGN

## Slide 44
Lateral Force Capacity of the Pile Group
Lateral load for 1 group is 80.25 kN.
The highest column height is 12.5 m. Others are 5 and 8 m.
Highest moment is M = 1003 kN.m
We assume cu is 200 kpa.
M/cuB3 = 5
From the figure, Qu/cuB2 = 5.5
Qu = 1100 kN
GEOTECHNICAL DESIGN

## Slide 45
Factor of safety per pile is 3.0.
Qall = 1100/3 = 367 kN
Group efficiency = 0.63
Lateral force capacity of the group = 0.63*367*8 = 1850 kN
1850 kN > 80.25 kN so our system is safe.
GEOTECHNICAL DESIGN

## Slide 46
Gadim Tosoyev
Cost EstImatIon

## Slide 47: Cost EstImatIon
240m
Total Cost = 56000 TL/m * 240 = 13.400.000 TL

## Slide 48: Cost EstImatIon
Excavation
Pier Column
Bridge Decks
Rebars
Foundation
Pile Driving
Formwork
Tendons
Earthmoving
Scaffolding

## Slide 49: Cost EstImatIon
Unit Cost For Concrete C50
(Ministry of Environment and Urban Planning of Turkey)

## Slide 50: Cost EstImatIon
Regression Analysis
Unit Cost (Ministry of Environment and Urban Planning of Turkey)
Unit price for Concrete C50 = 250 Tl/m3

## Slide 51: Cost EstImatIon
Quantity Take-off of Concrete Works

## Slide 52: Cost EstImatIon
Final Cost=17.181.501 TL

## Slide 53: THANKS FOR YOUR KIND ATTENTION
Post-Tensioning is Our Business
For further information please visit
www.ageaconstruction.io