## Slide 1: INTRODUCTION TO MATLAB
Hasan Gökhan Güler-Çağıl Kirezci
Lecture 3 – Loops, Surface Plot and Postprocessing
MIDDLE EAST TECHNICAL UNIVERSITY
Civil Engineering Department
Ocean Engineering Research Center

## Slide 2: Outline
Preprocessing
Control Flow: Loops
Surface Plot
Postprocessing
Summary

## Slide 3: Getting Data
DLMREAD: Gets data from ASCII-delimited file of numerical data (.dat) files.
Syntax:
variable=dlmread(‘filename.dat’, ‘delimiter’)
Delimiters: ‘,’ ‘;’ , etc.
Example:
loads=dlmread(‘loads.dat’, ‘;’)

## Slide 4: Getting Data
XLSREAD: Gets data from MS Excel sheets.
Syntax:
variable=xlsread(‘filename.extension’)
Extensions: .xls or .xlsx
Example:
loads=xlsread(‘loads.xlsx’)

## Slide 5: For Loop
A loop is a sequence of statements which is specified once but which may be carried out several times in succession. (Wikipedia)
For executes a group of statements a fixed number of times.
end
Counter = Initial Value such as 1
Counter <= N
Statements
YES
NO
increase Counter

## Slide 6: For Loop
for i=1:N Number of repetition
statements
end
Example: Find the summation of the elements of matrix A.
variable(i,j)
i: Row
j: Column

## Slide 7: While Loop
A while loop is a control flow statement that allows code to be executed repeatedly based on a given condition.

## Slide 8: While Loop
while condition Controls the repetition
statements
end
Example: Use while loop to find 5!, i.e., factorial of 5.

## Slide 9: Task 1
The design for the High Tower building you previously made in the class will be checked by Ministry of Construction. The control engineer requested the total load of the columns to compare with the calculations.
Your job is to write a code that finds total load
acting on the floor.
The data provided consists of x and y coordinates
of the columns, and the compressive loads (kN)
applied to these columns.
(0,0)
x
y
10m
10m
10m
10m
10m
10m
10m
10m

## Slide 10: Task 2
The control engineer found that some columns are not safe under the compressive loads. Write a code that investigates the safety of each column and gives a warning message if that column is not safe.
You are given that the compressive strength is 30MPa and the cross sections are 400x600 (in mm) for all columns.
Hint: To display a statement in the command window containing a variable you may use ‘fprintf’ function. The syntax is as follows:
>> fprintf(‘…… %i ……’, variable_name)
the place where you want to display the variable which is an integer

## Slide 11: Task 3
The control engineer requested the list of moments corresponding to each load with respect to x and y axes. Write a code that calculates total moment acting on the structure with respect to both axes
(0,0)
x
y
10m
10m
10m
10m
10m
10m
10m
10m

## Slide 12: Surface Plot
SCATTER3: 3-D Scatter Plot
Syntax:
scatter3(X,Y,Z)
Example:
x_coordinate = loads(:,1);
y_coordinate = loads(:,2);
force=loads(:,3);
scatter3(x_coordinate,y_coordinate,force)
loads(:,1)  All of the rows, first column in the variable loads.

## Slide 13: Surface Plot
BAR3: Plots 3-D bar chart
Syntax:
bar3(variable)

## Slide 14: Task 4
The control engineer requested a 3-D bar chart to visualize the forces. Your job is to plot forces at points (X1,Y1), (X1,Y2),…, (X5,Y5).
Y1
X1
X2
X3
X5
X4
Y2
Y3
Y4
Y5

## Slide 15: Resulting Graph for Task 4

## Slide 16: Prepare Report
DLMWRITE: Stores numeric or cell array in ASCII delimited file.
Syntax:
dlmwrite(‘filename.extension’, variable_name)
Example:
dlmwrite(‘axialforce.dat’, axial_force)

## Slide 17: Prepare Report
XLSWRITE: Stores numeric or cell array in MS Excel sheet.
Syntax:
xlswrite(‘filename.extension’, variable_name)
Example:
xlswrite(‘axialforce.xlsx’, axial_force)

## Slide 18: Class Exercise
Write a script that finds the root of the folllowing equation using Newton-Raphson formula. Consider absolute error, and an error tolerance of . Use initial guess as x=0.
Newton Raphson Method: